Housing Devices,

STANDARD FEATURES:

• Use with up to 10 ADA-1000 on the same

phone line or Voip interface

• Photoluminescent (glow in the dark)

instruction directory

• 10 Zone paper directory

• Tamper proof Hardware

• Engraved lettering not silk screened

• Brushed 16 ga. 304 #4 stainless steel face

plate, stainless steel enclosure

• Coordinate and control in-building rescue in

the event of an emergency

• Audible & Visual alert sounds when ADA-

1000 places call until ADA-ARCU-10 joins

conversation

• Full IBC, NFPA Life Safety 101,ADA, ASME

A17, B44 Elevator Code compliance

• Engraved 3” PUSH FOR HELP BUTTON

• Duplex communication

• 4 hours of full operation & standby upon loss

of power

• Momentary Dry Contact (ADA-1000)

• ADA Compliant Volume handset

DESCRIPTION:

The ADA ARCU-10 & ADA-1000 provides

hands-free audio and visual alarms to users,

Emergency Personnel, Offsite Communications

& complies with the Americans with Disabilities

Act. Installation is easily accomplished with

connections to an analog telephone line or

Voip Interface, AC power & the ADA-1000. In

the event of a power failure the ADA ARCU-10 &

The ADA-1000 each has an independent

battery backup system.

OPTIONAL FEATURES:

• Flush or Surface mounting (ADA-1000)

• Engraved Braille Signs

• Illuminated Area of Refuge or Area of

Rescue Assistance Signs with or without

Battery Back-Up

• Photoluminescent Area or Refuge or Rescue

Signage

2013 © Housing Devices, Inc. Visit our Website: www.housingdevices.com 800-392-5200

Wiring Diagram

ARCU-5

Operation of the ARCU

1. Solid lit LED (Ph o e, Mas ter A ,B, or Rescue

Services I ndicates Call in Progres s

2. Slow blink ing LED indicates Call on Hol d

4. Press yell owTALK/ HOLD but ton to call int o a

specific Mast er A or B. I f the green LED i s lit

you will join t he con v ion

5. Press Black TALK/HOLD butt on to call int oa

specific Area S tation ( ADA-1000). I f t he green

LED is li t you will join the con v ion.

6. Press TALK/HOLD bu tton again t o put t he call

on hold

7. Press RED Disconnect Call to Rescue Serv ces

Bu tton t o end ext ernal call. Any Area s tation

and Master A or B originally talk ing will rem ain

in the convers ation wit h this unit .

8. Hang up hand set to end calls to Area St ation

and other Mas ters in t he s yst em.

5

AREASTATION ZO NES

1 . _ __ _ _ ____ ___ _ __

2 . _ __ _ _ ____ ___ _ __

3 . _ __ _ _ ____ ___ _ __

4 . _ __ _ _ ____ ___ _ __

5 . _ __ _ _ ____ ___ _ __

6 . _ __ _ _ ____ ___ _ __

7 . _ __ _ _ ____ ___ _ __

8 . _ __ _ _ ____ ___ _ __

9 . _ __ _ _ ____ ___ _ __

1 0. _ _ _______ _ _____

Battery

AC

Analog Phone Line Plug-in

or ADA-IP Module Transformer

Wiring Notes

ARCU to ADA-1000 22-24 ga. 2 pair

twisted or Cat 5 or better cable.

Analog Phone line 1 pair 24-26 ga. or

Cat 5 or better cable.

ADA-IP Module 1 pair 24-26 ga. or

Cat 5 or better cable.

Plug-in Transformer use supplied

cable

Transformer to ADA-1000 connect

120Vac to the primary side of the

transformer per local electrical codes

and use 18 ga 1 pair twisted from the

secondary side of the transformer.

ARCU-5,10, ADA-1000 & ACS-2000

Disconnect

Call

Master

A

Master

B

1

2

3

4

5

AREA STATION ZONES

1. _______________

2. _______________

3. _______________

4. _______________

5. _______________

6. _______________

7. _______________

8. _______________

9. _______________

10. _______________

Battery

AC

Analog Phone Line Plug-in

or ADA-IP Module Transformer

Wiring Notes

ARCU to ADA-1000 22-24 ga. 2 pair

twisted or Cat 5 or better cable.

Analog Phone line 1 pair 24-26 ga. or Cat

5 or better cable.

ADA-IP Module 1 pair 24-26 ga. or Cat 5

or better cable.

Plug-in Transformer use supplied cable

ACS-2000 connect 120Vac power per local

code

ACS-2000 to ADA-1000 18ga 1 pair

twisted daisy chained up to 10 ADA-1000's

120 Vac

# Text boxes

Inc.

ARCU-10 & ADA-1000

ARCU-10

AREA STATION ZONES

1. _______________

2. _______________

3. _______________

4. _______________

5. _______________

6. _______________

7. _______________

8. _______________

9. _______________

10. _______________

HDI

AC

Model ADA-ARCU-10 Dimensions:

11.68”W x 12.63”H x 1.73”D

Model ADA-1000 Dimensions:

9”W x 9”H x Flush

9-1/4”W x 9-1/4”H x 2” Surface

SYSTEM OPERATION:

• All features of the ADA-1000 operate

the standard way.

• The ADA-ARCU-10 allows emergency

personnel to check the status of each

zone and to talk with each ADA-1000

on an individual basis or all of them

together.

• A lighted GREEN LED by Rescue

Services indicates that an emergency

call is in progress

• If an emergency call is in progress, by

lifting the handset on the ADA-ARCU

unit you automatically join the

conversation. At this point they can

place any or all ADA-1000 on hold by

pushing the Talk button a second time

to that unit, this will leave them talking

to the called party, or you can

disconnect the called party by pressing

the Disconnect Call , this will leave you

talking to the ADA-1000. (zones)

• If there is no emergency call in

progress you can call into any or all

ADA-1000 by pressing the

corresponding TALK button on the

unit.

Operation of the ARCU

1. Solid lit LED (Phone, Master A ,B, or Rescue

Services Indicates Call in Progress

2. Slow blinking LED indicates Call on Hold

3. Lift Handset

4. Press yellow TALK/HOLD button to call into a

specific Master A or B. If the green LED is lit

you will join the conversation

5. Press Black TALK/HOLD button to call into a

specific Area Station (ADA-1000). If the green

LED is lit you will join the conversation.

6. Press TALK/HOLD button again to put the call

on hold

7. Press RED Disconnect Call to Rescue Services

Button to end external call. Any Area station

and Master A or B originally talking will remain

in the conversation with this unit.

8. Hang up handset to end calls to Area Station

and other Masters in the system.

Help Requested

PUSH

FOR

HELP

ARCU-5,10, ADA-1000 & Transformer

ersat

Disco nn ect

Call

Ma ster

A

Ma ster

B

1

2

3

4

ersat

3. Lif t Hands et

n

i

HDI

H elp R eq ue ste d

PUSH

FOR

HELP

H elp Re qu est ed

PUSH

FOR

HELP

24

Vdc

120

Vac

H e lp R eq ue sted

PUSH

FOR

HELP

H elp Re qu este d

PUSH

FOR

HELP

24

Vdc

120

Vac

24

Vdc

120

Vac

H elp R equ est ed

PUSH

FOR

HELP

24

Vdc

120

Vac

24

Vdc

120

Vac

Wiring Diagram

ARCU-5

HDI

Operation of the ARCU

1. Solid lit LED (Phone, Master A ,B, or Rescue

Services Indicates Call in Progress

2. Slow blinking LED indicates Call on Hold

3. Lift Handset

4. Press yellow TALK/HOLD button to call into a

specific Master A or B. If the green LED is lit

you will join the conversation

5. Press Black TALK/HOLD button to call into a

specific Area Station (ADA-1000). If the green

LED is lit you will join the conversation.

6. Press TALK/HOLD button again to put the call

on hold

7. Press RED Disconnect Call to Rescue Services

Button to end external call. Any Area station

and Master A or B originally talking will remain

in the conversation with this unit.

8. Hang up handset to end calls to Area Station

and other Masters in the system.

Help Requested

PUSH

FOR

HELP

Help Requested

PUSH

FOR

HELP

Help Requested

PUSH

FOR

HELP

Help Requested

PUSH

FOR

HELP

Help Requested

PUSH

FOR

HELP

ACS-2000

Power Supply