Housing Devices, Inc.

ADA 121RM® Audio Visual Alert Remote

(For the Hearing & Visually Impaired)

STANDARD FEATURES:

(	Vandal Proof 18ga. 304 Stainless Steel

- Dual Audio & Visual Alarms for the Hearing & Visual Impaired

- Piezo Buzzer On-Off Switch

- .750” LED Strobe Light (110 Candela)

- High Volume (90dbA) Piezoelectric Surface Mount

- Flush Mount

- (	Remote Units available for Multiple Location installations (10 Max)

OPTIONS:

- White Powder Coating

DESCRIPTION:

The ADA 121RM® is a device used with the ADA-121, ADA-100, ADA-1000 & ADA-ARCU Area of Refuge System which enables people with visual and/or hearing impairments to be made aware of incoming telephone calls, when visitors to their residence are outside their front door and ringing the doorbell and Area of Refuge Alarms.

Awareness is stimulated via a very loud piezoelectric buzzer and a  flashing

strobe light.  The sound emitted can be switched ON or OFF.

ADA-121RM

4.75”h x 6.5”w x .375”d

SYSTEM OPERATION:

Activation is accomplished by the ADA-121 or  a 24 volt Vdc input.

Mounting SYSTEMS & Dimensions

The ADA-121 is designed to be mounted

surface or flush using a 3 gang old or new

work box (flush mount), or a 3 gang Wiremold

box (surface mount)

# Text boxes

RESET

POWER

TALK      LISTEN   TROUBLE

1ST FLOOR

NORTH

1ST FLOOR

SOUTH

2ND FLOOR

NORTH

2ND FLOOR

###### SOUTH

ELEV LOBBY

3

3

3

2

4

1

Master Station

Relay Card Cabinet

with

Control Board

Relay Cards

Battery Backup Cabinet

With

ADA-35 Amplifier

ADA-24V transformer

Battery Charger

Batteries

##### OR

Amplifier Cabinet

With

ADA – 35 Amplifier

PUSH

FOR

HELP

HELP  COMING

HELP   REQUESTED

PUSH

FOR

HELP

HELP  COMING

HELP   REQUESTED

PUSH

FOR

HELP

HELP  COMING

HELP   REQUESTED

Area Station

Area Station

Area Station

5